# Operation Instruction for Short-distance Gree-Smart

http://www.gree.com/english/downloadcenter/ihome_jsp_catid_2840.shtml

This software is applicable to: android 4.0 or above, ios7 or below

Applicable model: U-Smart

1. Install application: Download the application to your phone and install it by following the prompts. You may also enter “Settings”→”Application”→”Application manager”, then press APK to install.

Installation package for I-phone can be downloaded from the Apple Store.

2. First start: First of all, switch on the air conditioner. Then turn on the wifi function of your smart phone. Scan the network and then connect to the network of air conditioner, which is named as: “gree-xxxxx” (x can be a number or a letter from a to f). Original password: “12345”. Finally, press the startup icon and wait for it to power up. The Room page will be shown directly after the logo.

3. Room page: As shown in figure 1-1, press “Refresh” if air conditioner is not found. Press the power on/off button to turn on/off the air conditioner. Press the picture to enter the main control page of air conditioner.

Fig 1-1                          Fig 1-2

4. Functions on control page: As shown in figure 1-2, press the word “AUTO”, then Mode buttons will be displayed for mode switching, as in figure 1-3; Press the figure of temperature, then a temperature selector will be displayed. Slide up and down to adjust the temperature, as in figure 1-4; Press the fan icon, then a speed regulator will be displayed. Touch and slide it to adjust the fan speed, as in figure 1-5; Press the menu button, i.e. the icon  in the bottom right corner of the screen, then you may enter the corresponding page as you need, as in figure 1-6.

Fig 1-3						Fig 1-4

Fig 1-5                         	Fig 1-6

5. Page of settings: As shown in figure 1-7, this page displays the current network status and version of the software. Press “Settings” and then input the username “admin” and password “admin” to enter the page of network setting.

6. Page of air conditioner settings: As shown in figure 1-8, there are 3 functions in this page: connect AC to the router, change AC’s username and password; change the room page.

How to connect AC to the router?

- Press “Network type” and select the wireless network of your family.

- As to the net name, select the name of your home router. Safe mode is auto.

- Key refers to the password of your router. Press “Sure” to connect AC to the router.

- By this time, your phone is still inactive in the network of air conditioner. You can connect wifi of your phone to the router’s network. Or you can wait 20 seconds for your phone to switch to the router’s network automatically.

How to change AC’s username and password: Move the cursor to the input box of user name and change it. Move the cursor to the input box of new password and then the input box of confirm password to change it. Press “Sure” to complete the change.

How to change AC’s name: Move the cursor to the input box of room name and change it. Press “Sure” to save the setting.

Fig 1-7                            	Fig 1-8

7. Page of preset: As shown in figure 1-9, set the time for timer ON and timer OFF. Press “Period” to set the period for timer ON/OFF.

Fig 1-9                 		Fig 1-10					Fig 1-11

- 8. Page of functions: As shown in figure 1-12, functions including Light, Purify, X-fan, etc. can be set.

Functions of Light, Purify, X-fan and Turbo adopt state switch. Pressthe corresponding button to switch the status between On and Off.

There are several states for functions of Mute, E-heater, Humidify and Air exchange. Press the corresponding function to enter the next page for state selection, as shown in figure 1-13 and figure 1-14.

Fig 1-12                    	Fig 1-13

Fig 1-14                       	Fig 1-15

- 9. Page of air swept: As shown in figure 1-16, left & right swing and up & down swing can be set on this page. Press the arc to set the area of air swept. If the two slide blocks are separate, air swing will take place in the indicated area. If the two slide blocks are next to each other, air swing will be fixed at an angle.

Fig 1-16                      	Fig 1-17

10. Page of advanced functions: As shown in figure 1-17, advanced functions include Sleep curve, Regional swing, Noise and Power saving. The function of power saving can be set by directly pressing on the state switch. Pressing on the other functions will enter into a subsequent page.

11. Page of sleep curve: The change of indoor temperature within 8 hours can be set on this page. If you select DIY mode, you can set the temperature by yourself, as shown in figure 1-18. The curves of other 3 sleep modes are already set by the system, as shown in figure 1-19.

Fig 1-18					 	Fig 1-19

12. Page of regional swing: On this page, you can set the room size as shown in figure 1-20 and air flow posiiton as shown in figure 1-21.

Press “Air flow position” to enter a subsequent page. At the top of the grid, there is an air conditioner, which can be adjusted left and right. Turn on the function of regional swing, then you can adjust the position of people within the grid. System will adjust the air swept area according to the On/Off status of “Avoid people”.

Fig 1-20                      	Fig 1-21

13. Page of noise: On this page, you can set the degree of noise. Press “Noise degree in cooling” to set noise degree in cooling mode. Press “Noise degree in heating” to set noise degree in heating mode. Air conditioner will adjust fan speed according to the set noise degree. However, fan speed won’t be displayed here.

Fig 1-22

Operation steps of each function:

1. Turn on/off the air con: Press  to turn on or off the air conditioner.

2. Switch modes: On the control page, press the word of a certain mode and then buttons of different modes will be displayed. Press any of them to switch to a different mode.

3. Set temperature: Press the temperature and then a temperature selector will be displayed. Slide the temperature selector to set a temperature.

4. Set fan speed: Press the running fan and then a fan speed regulation will be shown. Press or slide the regulator to set fan speed. Turbo fan speed can only be set in cooling or heating mode. In drying mode, only low fan speed is available.

5. Connect AC to the router: “Room page” → ”Control page” → ”Menu” → ”Network setting” → “Press Settings” → ”Input username and password admin ” → ”Network type: family wireless network” → ”Network name: router’s name” → ”Safe mdoe: auto” → ”Key: rouetr’s password” → ”Sure”

6. Change air conditioner’s username and password: “Room page” → ”Control page”→ ”Menu” → ”Network setting” → ”Press Settings” → ”Input username and password admin” → ”Input the new login name, new password and confirm password” → ”Sure”

7. Change air conditioner’s name: “Room page” → ”Control page” → ”Menu”→ ”Network setting” → ”Press Settings” → ”Input username and password admin” → “Edit the air conditioner’s name” → “Sure”

8. Timer ON: “Room page” → ”Control page” → ”Menu” → “Preset” → “Timer ON” → “Set time” → “Set period” → “Save”

9. Timer OFF: “Room page” → ”Control page” → ”Menu” → “Preset” → “Timer OFF” → “Set time” → “Set period” → “Save”

10. Light: “Room page” → ”Control page” → ”Menu” → “Functions”, press state switch to turn on/off the light.

11. Purify: Press state switch to turn on/off purification.

12. X-fan: Press state switch to turn on/off X-fan.

13. Turbo: Press state switch to turn on/off turbo. Turbon can only be turned on in cooling or heating mode. If Turbo function is on, Mute and Noise functions will be disabled.

14. Mute: “Room page” → ”Control page” → ”Menu” → “Functions” → “Mute”, press the state switch or select the options of ON and OFF. If Mute function is on, Turbo and Noise functions will be disabled.

15. E-heater: Enter the page of E-heater and set the status of E-heater. It is only available in heating mode.

16. Humidify: Enter the page of Humidify and set the status of Humidify. This function is not available in drying mode.

17. Air exchange: Enter the page of Air exchange and set the status of Air exchange.

18. Left & right swing: “Room page” → ”Control page” → ”Menu” → “Swept”, pull the slide blocks to adjust the area of left & right swing. If the two blocks are next to each other, air swing will be fixed at an angle. If they are separate, air swing will take place in the indicated area. The maximum area of air swept is determined according to the position of ait conditioner.

19. Up & down swing: Pull the slide blocks to adjust the area of up & down swing. If the two blocks are next to each other, air swing will be fixed at an angle. If they are separate, air swing will take place in the indicated area. If up & down swing is set, regional swing will be disabled.

20. Sleep curve: “Room page” → ”Control page” → ”Menu” → “Advanced” → “Sleep curve”, select an applicable curve to enable the sleep mode. You may select DIY mode to adjust the sleep curve by yourself. If sleep mode is on, Mute function will be on automatically.

21. Regional swing: “Room page” → ”Control page” → ”Menu” → “Advanced” → “Regional swing”, adjust the position of air conditioner and people. System will determine the air swept area according to the On/Off status of “Avoid people”.

22. Noise: “Room page” → ”Control page” → ”Menu” → “Advanced” → “Noise”, press “Noise degree in cooling” to set noise degree in cooling mode. Press “Noise degree in heating” to set noise degree in heating mode. Air conditioner will adjust fan speed according to the set noise degree. However, fan speed won’t be displayed.

23. Power saving: “Room page” → ”Control page” → ”Menu” → “Advanced”, press the state switch to turn on/off the function of power saving.